APR Report

1. CTSRPT

###############################################################
# Generated by: Cadence Encounter 14.27-s035_1
# OS: Linux x86_64(Host ID eecad32.eas.asu.edu)
# Generated on: Wed Nov 30 20:34:30 2016
# Design: simon32_64
# Command: reportClockTree -report simon32_64.ctsrpt -clk clk -postRoute
###############################################################
###############################################################
# Complete Clock Tree Timing Report
#
# CLOCK: clk
#
# Mode: postRoute
#
# Delay Corner information
# Analysis View : default_setup_view
# Delay Corner Name : delayCorner_slow
# RC Corner Name : RC_corner_25
# Analysis View : default_hold_view
# Delay Corner Name : delayCorner_fast
# RC Corner Name : RC_corner_25
###############################################################

Nr. of Subtrees : 1
Nr. of Sinks : 3041
Nr. of Buffer : 93
Nr. of Level (including gates) : 6
Root Rise Input Tran : 0.1(ps)
Root Fall Input Tran : 0.1(ps)
No Driving Cell Specified!
Max trig. edge delay at sink(R): k0_reg[13][1]/CLK 151.2(ps)
Min trig. edge delay at sink(R): k2_reg[6][7]/CLK 110.1(ps)

        (Actual) (Required)
Rise Phase Delay : 110.1~151.2(ps) 0~10(ps)
Fall Phase Delay : 121.7~165.9(ps) 0~10(ps)
Trig. Edge Skew : 41.1(ps) 16(ps)
Rise Skew : 41.1(ps)
Fall Skew : 44.2(ps)
Max. Rise Buffer Tran : 55.4(ps) 200(ps)
Max. Fall Buffer Tran : 44(ps) 200(ps)
Max. Rise Sink Tran : 67.9(ps) 200(ps)
Max. Fall Sink Tran : 54.3(ps) 200(ps)
Min. Rise Buffer Tran : 9.7(ps) 0(ps)
Min. Fall Buffer Tran : 9.7(ps) 0(ps)
Min. Rise Sink Tran : 4.9(ps) 0(ps)
Min. Fall Sink Tran : 4.1(ps) 0(ps)

view default_setup_view : skew = 41.1ps (required = 16ps)
view default_hold_view : skew = 41.1ps (required = 16ps)

***** NO Max Transition Time Violation *****

***** NO Min Transition Time Violation *****

***** NO Max_Fanout Violation *****

***** NO AC Irms Limit Violation *****

**** Sub Tree Report ****
OUTPUT_TERM: clk [0(ps) 0(ps)]

Main Tree:
     nrSink : 3041
     Rise Delay	: [110.1(ps) 151.2(ps)]
     Rise Skew	: 41.1(ps)
     Fall Delay	: [121.7(ps) 165.9(ps)]
     Fall Skew	: 44.2(ps)

  Main Tree from clk w/o tracing through gates:
     nrSink : 3041
     nrGate : 0
     Rise Delay [110.1(ps) 151.2(ps)] Skew [41.1(ps)]
     Fall Delay [121.7(ps) 165.9(ps)] Skew=[44.2(ps)]

2. Geom.rpt
###############################################################
# Generated by: Cadence Encounter 14.27-s035_1
# OS: Linux x86_64(Host ID eecad32.eas.asu.edu)
# Generated on: Wed Nov 30 20:45:10 2016
# Design: simon32_64
# Command: verifyGeometry
###############################################################

Begin Summary ...
  Cells : 0
  SameNet : 0
  Wiring : 0
  Antenna : 0
  Short : 0
  Overlap : 0
End Summary

No DRC violations were found

3. Conn.rpt

###############################################################
# Generated by: Cadence Encounter 14.27-s035_1
# OS: Linux x86_64(Host ID eecad32.eas.asu.edu)
# Generated on: Wed Nov 30 21:46:35 2016
# Design: simon32_64
# Command: verifyConnectivity -type all -error 1000 -warning 50
###############################################################
Verify Connectivity Report is created on Wed Nov 30 21:46:35 2016

Begin Summary
    Found no problems or warnings.
End Summary

4. Gate and Area

simon32_64 Gates=142221 Cells=35834 Area=99532.2 um^2